## Slide 1
FINAL PRESENTATION
TrackShift
Beyond Curve Fitting: Probabilistic Tyre Intelligence for F1 Strategy
Real FastF1 telemetry
Kalman-filter core
Live pit-wall dashboard
A risk-aware pit-wall co-pilot built on public F1 data

## Slide 2
THE PROBLEM
A lap-time guess isn't a strategy
“A pit wall doesn’t need to know a lap will be 94.5 seconds.
It needs an answer: will this tyre survive to the next pit window?”
A single MAE score
hides sudden cliffs — a model can be accurate on average and still miss the drop-off.
Real tyre sensors are private
carcass temperature, pressure and slip live on team servers, never broadcast.
Every circuit is different
the same compound wears at a different rate at Monaco than at Silverstone.
TrackShift
2

## Slide 3
WHAT'S NEW
Three ideas that aren't curve-fitting
Probabilistic, not deterministic
A two-state Kalman filter outputs a mean forecast, a 70%/90% uncertainty band, and a calibrated probability of crossing the cliff — not one guessed number.
Virtual sensors, transparently labelled
Six physics-informed proxies (thermal, slip, lateral load…) stand in for the private team CAN-bus data that no one can access — and the code says so.
Provenance is never hidden
Every input is tagged real telemetry, published prior, or reconstructed proxy. Demo mode is always visibly labelled ‘illustrative’.
TrackShift
3

## Slide 4
HOW IT RUNS
Two phases: train once, adapt every weekend
Pre-Race — Training
1
Pull historical FastF1 race laps for every 2025 Grand Prix
2
Clean, green-flag filter, and fuel-correct every lap
3
Fit global Kalman priors from robust median slopes
4
Save the reusable state-space model bundle
Race Weekend — Live Usage
1
FP1→FP3 clean laps arrive as they're driven
2
Each lap sequentially updates the posterior state
3
Model forecasts pace loss + cliff probability ahead
4
Dashboard surfaces a pit window recommendation
TrackShift
4

## Slide 5
DATA PIPELINE
From raw laps to a clean signal
1
Filter
Keep only green-flag, dry-compound, in-stint laps — drop pit in/out and safety-car laps.
→
2
Fuel-correct
Remove the ~110kg fuel burn-off effect so cars don't look faster just from getting lighter.
→
3
Baseline
Median of laps 2–5 sets the ‘fresh tyre’ reference pace for that stint.
→
4
Degradation Δ
Every lap becomes clip(lap time − baseline, ≥ 0) — the observed pace-loss signal.
FUEL CORRECTION FORMULA
Fuel_Corrected_LapTime = LapTime − Fuel_Weight(kg) × Penalty
Penalty ≈ 0.018 + 0.0015 × downforce + 0.0012 × braking · Fuel_Weight decays linearly, 110kg → 0kg over the race
TrackShift
5

## Slide 6
FEATURE ENGINEERING
Six proxies stand in for private CAN data
Thermal Stress
Track-temperature deviation from a 34°C reference
Pressure Deviation
Modelled drift from a 21.5 psi nominal pressure
Slip Energy
Traction, tyre-stress and abrasion combined
Lateral Load
Cornering-load index from track profile × downforce
Brake Thermal
Braking-severity index scaled by track heat
Aero Load
Downforce-driven vertical load on the contact patch
These are physics-informed proxies built from public track and weather data — not measured sensor values. The dashboard's virtual-sensor panel lets an engineer see and tune every input.
TrackShift
6

## Slide 7
THE MATH
Three formulas carry the whole model
Latent-State Update
Two-state Kalman filter
x = [ degradation, rate ]
predict: x' = Fx + w
update: Joseph-form covariance
Innovation clipped to ±2.8σ so one bad lap is never read as a tyre cliff.
Cliff Probability
Normal CDF risk score
P(cliff) = 1 − Φ( (1.5 − μ) / σ )
Turns a point forecast into a decision-ready probability of exceeding the 1.5s cliff threshold.
Wear-Load Multiplier
Composite of 11 factors
m = clip( 0.70 + 0.30 · Σ wᵢ·scoreᵢ, 0.70, 1.55 )
Weighted across thermal, pressure, slip, lateral, brake, vertical, camber, toe, differential, brake-bias and aero.
Sensor-proxy choices follow Pacejka's slip–load–camber framework (Tire and Vehicle Dynamics). Wear weights are declared priors, nudged conservatively by clean practice-session evidence — never fitted as exact physical constants.
TrackShift
7
Notes: Deeper detail if asked: - Prior fitting: robust MEDIAN slope across historical stints (not mean, so outlier stints don't skew it), plus MAD (median absolute deviation x 1.4826) sets observation noise. - Weekly update: prior_weight_i *= (1 + learning_rate * (evidence_i - 1)), renormalized so total weight stays fixed -- prevents overfitting to a handful of FP1 laps. - Farroni et al.'s TRICK tyre/road thermal-and-wear work is a relevant secondary reference for the thermal/wear layer -- track down the exact edition/DOI before citing it in a formal paper; don't present the secondary summary as if it were the primary source. - Joseph-form covariance update is used specifically because it's numerically robust and guarantees the covariance stays positive semi-definite, which a naive update doesn't guarantee.

## Slide 8
SOURCE OF TRUTH
Three data tiers, honestly labelled
REAL
FastF1 broadcast telemetry
Lap times, sectors, weather and telemetry pulled from F1's live-timing feed — the same stream behind official broadcast graphics. Lap and sector times are treated as ground truth.
PUBLISHED PRIOR
Pirelli per-circuit stress ratings
Traction, abrasion, lateral load and evolution scores (1–5) from Pirelli's own circuit engineering ratings — the same briefing shared with every team, not a fan graphic.
RECONSTRUCTED
Virtual sensor proxies
Thermal stress, slip energy and pressure deviation approximate private team CAN-bus data — public to no one, clearly reconstructed, never disguised as measured.
Demo mode always shows a visibly labelled “Illustrative demo” stint — never real data passed off as real.
TrackShift
8
Notes: If pushed on Pirelli sourcing: this is Pirelli's own numeric 1-5 engineering classification for traction/grip/abrasion/evolution/stress/braking/lateral, the same data given to every team pre-weekend, not the colorful fan-facing compound-selection graphic. Track down the specific Pirelli pre-race technical/media page the numbers were sourced from before an external submission, and cite that primary page directly. If pushed on FastF1 trust: 'unofficial' describes licensing status, not data quality -- FastF1 pulls from livetiming.formula1.com, the real F1 live-timing feed, and its own docs call lap/sector times 'absolute truth'. What it does NOT give us is private team CAN-bus data (tyre pressure, carcass temp, suspension load) -- that gap is exactly what the virtual sensor layer exists to approximate.

## Slide 9
THE PRODUCT
A pit-wall view, not a spreadsheet
STRATEGY OVERVIEW
Tyre Stage
Optimal Grip
Recommendation
Maintain Pace
Cliff Age
Lap 21
Pit Window
Lap 19–21
Pace Loss
0.23 ± 0.16s
Chart: Live weekend posterior & race forecast
| 1 | 5 | 9 | 13 | 17 | 21 | 25
Forecast mean | 0.05 | 0.18 | 0.32 | 0.55 | 0.95 | 1.55 | 2.3
Live Weekend
FP1→FP3 laps update the posterior in real time
Live Simulation
Animated lap-by-lap replay with track-stress map
Post-Race Validation
Forecast vs. actual, with 90% band coverage
TrackShift
9

## Slide 10
RESULTS
Validated across a full season
17
Grands Prix covered
21
Drivers tracked
748
Stints modelled
15,949
Clean racing laps analysed
0.33s
Laps-weighted forecast MAE
87%
Stints reaching a detected cliff
Every figure above comes straight from the pipeline's own output files — no cherry-picking, nothing invented for the slide.
TrackShift
10

## Slide 11
ENGINEERING CHOICES
Built for the pit wall, not a training cluster
No GPU — by design
The entire online model is a 2×2 Kalman filter in NumPy. There is no matrix large enough for a GPU to accelerate, and the transfer overhead would make it slower, not faster.
A pit wall needs sub-second updates on a laptop — not a training cluster.
Interpretable over black-box
Earlier experiments explored ensemble and neural approaches to degradation. We moved to a state-space model an engineer can audit lap by lap.
Every number traces to a formula — nothing is hidden in a learned layer.
TrackShift
11
Notes: If asked about leftover files (ultimate_neural_f1_degradation.parquet, bayesian_deg_model.ipynb): be upfront -- we explored other approaches (ensemble/neural) before pivoting to the Kalman filter, specifically because a state-space model is more interpretable and auditable for a pit-wall decision tool. Don't get caught contradicting this if a mentor has browsed the repo history.

## Slide 12
REFERENCES
Grounded in published work, not guesswork
Pacejka, H. B. — Tire and Vehicle Dynamics. Physical reference for how slip, load and camber shape the contact patch and heat generation; grounds the choice of thermal/slip/lateral sensor proxies.
Farroni et al. — TRICK tyre/road thermal and wear modelling. A relevant secondary reference for the thermal-wear layer.
FastF1 (unofficial client) — pulls real lap, sector, weather and telemetry data from F1's live-timing feed.
Pirelli — published per-circuit engineering stress ratings (traction, abrasion, lateral load, evolution), the same briefing shared with every team.
Not a black box.
A transparent, risk-aware co-pilot for the pit wall.
Thank you
TrackShift
12